## Slide 1: Chromatography
Instrumental Analysis

## Slide 2
Key Principles of Chromatography:
Differential Affinity: Components of the mixture exhibit different affinities for the stationary phase. Those with stronger interactions spend more time in the stationary phase, while those with weaker interactions move faster with the mobile phase.
Distribution (Partition) Coefficient: The distribution coefficient represents the ratio of the concentration of a component in the stationary phase to its concentration in the mobile phase. A higher DC indicates a stronger affinity for the stationary phase.

## Slide 3
Retention Factor: The retention factor (Rf) is a measure of how long a component remains in the stationary phase compared to the mobile phase.

## Slide 4
Resolution: Resolution (Rs) is a measure of the ability of a chromatographic system to separate two components.

## Slide 5
Types of Chromatography:
Normal Phase Chromatography (NPC): The stationary phase is polar, and the mobile phase is nonpolar. Components with higher polarity interact more strongly with the stationary phase and elute later.
Reverse Phase Chromatography (RPC): The stationary phase is nonpolar, and the mobile phase is polar. Components with lower polarity interact more strongly with the stationary phase and elute later.
Ion Exchange Chromatography (IEC): The stationary phase contains charged groups that interact with ions of opposite charge in the sample. Components with higher charge interact more strongly with the stationary phase and elute later.
Size Exclusion Chromatography (SEC): The stationary phase consists of porous beads with different pore sizes. Larger molecules are excluded from smaller pores and elute earlier, while smaller molecules enter smaller pores and elute later.
Affinity Chromatography: The stationary phase is modified with a ligand that has a specific affinity for a target molecule. The target molecule binds to the stationary phase and elutes later than non-binding components.

## Slide 6
Feature | Low-Pressure Liquid Chromatography (LPLC) | High-Pressure Liquid Chromatography (HPLC)
Operating Pressure | Low (typically < 5 bar or < 70 psi) | High (typically 50–600 bar; up to 1200 bar in UHPLC)
Driving Force | Gravity or a low-pressure pump | High-pressure pump system
Column Type | Larger particle size (20–100 µm), longer columns | Smaller particle size (3–10 µm), shorter columns
Flow Rate | Usually slower and less precise | Precisely controlled and faster
Resolution | Lower—less efficient separation | Higher—greater separation efficiency and sharper peaks
Detection Sensitivity | Moderate | High—suitable for trace analysis
Applications | • Preparative purification of biomolecules (proteins, peptides, etc.) • Ion exchange or gel filtration (size-exclusion chromatography) | • Analytical quantification and identification of small molecules, drugs, metabolites, etc. Reverse-phase HPLC
Instrumentation Complexity | Simple and inexpensive | Complex and more expensive
Sample Capacity | Handles larger sample volumes | Handles small sample volumes
Common Use Cases | Biochemistry, protein purification, desalting | Analytical chemistry, pharmaceutical analysis, quality control
1 bar = 14.5038 psi (pounds per square inch)
Comparison between Low-Pressure Liquid Chromatography (LPLC) and High-Pressure Liquid Chromatography (HPLC):

## Slide 7
Feature | FPLC (Fast Protein Liquid Chromatography) | HPLC (High-Performance Liquid Chromatography)
Operating Pressure | Low to moderate (typically < 5 MPa or < 50 bar) | High (50–600 bar, up to 1200 bar in UHPLC)
Purpose | Purification and separation of proteins, peptides, and other biomolecules | Analytical or preparative separation of small molecules, such as drugs and metabolites
Stationary Phase (Column) | Larger particle size (20–100 µm), soft or gel-based matrices (e.g., Sepharose, Superdex) | Smaller particle size (3–10 µm), rigid silica-based particles
Mobile Phase (Solvent) | Aqueous buffers (mild conditions, pH-controlled) to maintain protein stability | Often uses organic solvents (e.g., acetonitrile, methanol) and sometimes pH gradients
Sample Type | Biomolecules that are sensitive to denaturation (proteins, nucleic acids) | Small organic molecules, drugs, or metabolites
Detection Methods | UV (280 nm for proteins), conductivity, pH | UV (typically 210–254 nm), fluorescence, mass spectrometry
Flow Control | Usually, low-pressure pumps designed for biocompatibility | High-pressure pumps designed for solvent resistance and precision
Comparison between FPLC (Fast Protein Liquid Chromatography) and HPLC:

## Slide 8
Temperature Conditions | Usually run at low or ambient temperature to preserve biomolecules | Often run at ambient or slightly elevated temperatures
Column Material Compatibility | Biocompatible (e.g., plastic, stainless steel coated with inert materials) | Stainless steel (solvent-resistant, not always biocompatible)
Applications | Protein purification, desalting, buffer exchange, ion-exchange, affinity chromatography | Quantitative analysis, quality control, and purity testing of chemical compounds
System Example | GE ÄKTA, Bio-Rad NGC | Agilent 1260, Shimadzu Nexera, Waters Alliance
Feature | FPLC (Fast Protein Liquid Chromatography) | HPLC (High-Performance Liquid Chromatography)
Comparison between FPLC (Fast Protein Liquid Chromatography) and HPLC:

## Slide 10
FPLC

## Slide 11
Ultra-performance liquid chromatography (UPLC) is a groundbreaking advancement in liquid chromatography (HPLC) technology that offers significant improvements in speed, resolution, and sensitivity.

## Slide 12
UPLC

## Slide 13
UPLC

## Slide 15
Feature | HPLC | GC | LC-MS | FPLC | UPLC
Mobile phase | Liquid | Gas | Liquid | Liquid | Liquid
Stationary phase | Solid | Solid | Solid | Solid | Solid
Sample type | Non-volatile compounds | Volatile compounds | Non-volatile compounds | Biopolymers | Non-volatile compounds
Resolution | High | Medium | High | Medium | High
Speed | Moderate | Fast | Moderate | Moderate | Fast
Efficiency | High | High | High | High | High
Sensitivity | High | High | Very high | High | High
Applications | Pharmaceutical analysis, environmental analysis, food science, biochemistry | Pharmaceutical analysis, environmental analysis, petrochemical analysis | Pharmaceutical analysis, environmental analysis, food science, biochemistry | Protein purification, nucleic acid purification, enzyme purification | High-throughput analysis in pharmaceutical, environmental, and food industries
Comparative Analysis Details